The Lunascan Project - MOONWATCH - Team Report 
June 26, 2012

| TARGETS: | Eastern Limb | Sunset on Ptolemaeus |
| --- | --- | --- |

BOS 20:44:00 Q Approx 8:44 PM CREW Fran Ridge, Lorelei Barnes, Earnie Lerker, Zach Lerker MISSION PLAN: Range 370,129 km / 229,850 mi Colongitude 3.6 Lunation 7.37 days Illumination 48.4% Simrange 574 miles Time fix at 1H 51m CUT = 7m 19s elapsed Time fix at 3H 34m CUT = 1h 50m 13s Confirmed by extrapolation Good imaging with poor WWV signal due to noise level. Tuneable receiver near van. Camera 1 mini finder Camera 2 Cargo cams (1 &2) Camera 3 LPI/VMA graphics. (LPI not used) Camera 4: SSI/CCD/ C-8. . . CAMERAS: CAMERA ONE POSITION ON QUAD * Finder: mini cam CAMERA TWO POSITION * Cargo cameras color minicam & night vision CAMERA THREE POSITION Compaq Presario sr1218nx computer (1) Digital to Analog Converter 1; TEP-100 Elite Pro II VIRTUAL MOON ATLAS graphics CAMERA FOUR POSITION Dell computer Digital to Analog Converter 2: TEP-100 Elite Pro II Aperture video recorder DVR2 No graphics used All camera outputs to Quad / VHS1 / Q Select DVR1 SSI Camera CCD, (Celestron Neximage Solar System Imager / Charge Coupled Device) OPTICS, prime focus. 5 mm VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 LPI Camera Not used CMOS, (Meade Lunar Planetary Imager / complementary metal oxide semiconductor) OPTICS, prime focus. 6 mm. VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 Celestron C-8 SCT 8” optical tube 2032 mm f/l F10 Resolution at lunar range = 0.68 / .81086 mi or 4281.36469 feet (30.19' X 60 = 1811.4" /.68' resol = factor of 2663.82353 2160 miles / 2663.82353 = .81086 mi resolution) 0.621 mi/km 1 m = 3.28 ‘ CONFIG No diagonal or binoc viewer. Extended hand control DOB Driver II REPORT NOTES Good recordings except for problems after 1 hour with slipage of belt on elevation. Good A/V on VCR1,3, DVR2 PPI Marker on cam 1 mon didn’t work on black screen. SUGGESTIONS . Aperture video VHS3 used on Cargo cams 1. Compaq Presario sr1218nx XP home, dvd rom, cd burner, 2.67 GHZ processor, 760 mb RAM, 80 GB hard drive T