The Lunascan Project - MOONWATCH - Team Report 
July 11, 2012

| TARGETS: | Western Hemisphere | Multiple Targets |
| --- | --- | --- |

Grab from 03:34:43 BOS = 03:00:45 Quad CREW Fran Ridge MISSION PLAN: Date: 2012-07-11 02:00:00 Distance: 400114Km / 248,470 miles Apparent diameter: 29.87' Colongitude: 177.7° Phase: 268.2° Lunation: 21.62 days Illumination: 48.4% Simrange 600 miles Camera 1 mini finder Camera 2 Cargo cams (1 &2) Camera 3 LPI/VMA graphics. (LPI not used) Camera 4: SSI/CCD/ C-8. . . CAMERAS: CAMERA ONE POSITION ON QUAD * Finder: mini cam CAMERA TWO POSITION * Cargo cameras color minicam & night vision CAMERA THREE POSITION Compaq Presario sr1218nx computer (1) Digital to Analog Converter 1; TEP-100 Elite Pro II VIRTUAL MOON ATLAS graphics left EM Datalogger right (new) CAMERA FOUR POSITION Dell computer Digital to Analog Converter 2: TEP-100 Elite Pro II Aperture video recorder DVR2 No graphics used All camera outputs to Quad / VHS1 / Q Select DVR1 SSI Camera CCD, (Celestron Neximage Solar System Imager / Charge Coupled Device) OPTICS, prime focus. 5 mm VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 LPI Camera Not used CMOS, (Meade Lunar Planetary Imager / complementary metal oxide semiconductor) OPTICS, prime focus. 6 mm. VGA resolution (640x480) color ¼” CMOS chip 30 fps Compression 1420 Celestron C-8 SCT 8” optical tube 2032 mm f/l F10 Resolution at lunar range = 0.68 / .81086 mi or 4281.36469 feet (30.19' X 60 = 1811.4" /.68' resol = factor of 2663.82353 2160 miles / 2663.82353 = .81086 mi resolution) 0.621 mi/km 1 m = 3.28 ‘ CONFIG No diagonal or binoc viewer. Extended hand control DOB Driver II REPORT NOTES Moderate imaging (haze) with limb less than sharp No WWV signal due to noise level. Tuneable receiver near van. Street position Venus and Jupiter imaged at EOS EMF datalogger injection with VMA graphics was very successful Good A/V on VCR1,3, DVR2 Quad 03:00:45Q BOS w/o Moon on Cam 4 03:04:28Q Target acq at 3:47:00 elapsed 04:36:26Q Loss of target (Moon) when mission switched to Venus 04:41:04Q Flash of Venus 04:41:41Q Steady live image of Venus 1:46:00 elapsed Capture 064 at 1:40:54 elapsed DVR2 Venus flash at 1:41:07 elapsed Steady at 1:41:44 elapsed Jupiter acq at 1h46m25s elapsed: Time fix therefore is Cam 4 start as 2:59:57 Q VHS1 48 secs later at 3:00:45Q Analysis of DVR as follows: LOS at 1h02m10s elapsed Regain at 1h07m00s elapsed . SUGGESTIONS Inject manual time fix notation with WT and scanner. Use binoc e/p adaptor to lower light level and have e/p for finding targets. Aperture video VHS3 used on Cargo cams Video splitter on finder so that night vision of sky can be recorded on Cam 1 position on Q 1. Compaq Presario sr1218nx XP home, dvd rom, cd burner, 2.67 GHZ processor, 760 mb RAM, 80 GB hard drive T